## Slide 1: Project Area : LOCOMOTION OF QUADRUPED ROBOT Project Topic : QUADRUPED ROBOT – SEARCH AND RESCUE
SAINTGITS
COLLEGE OF ENGINEERING
(AUTONOMOUS)
LEARN . GROW . EXCEL
Supervisor
Name : Er. CHINN MOHANAN
Designation : Assistant Professor
Presented By :
SANJITH SAJI(MGP22URB085)
SEFIN SURESH(MGP22URB086)
P.ARJUN(MGP22URB077)
S6 RBB
SAINTGITS College of Engineering
Mini Project FIRST REVIEW

## Slide 2
LEARN . GROW . EXCEL
Contents
Introduction
Literature Review
Methodology
Theoretical Calculations
Control Circuit
Analysis
Budgeting
Roadmap
Reference

## Slide 3
LEARN . GROW . EXCEL
INTRODUCTION
Our quadruped robot is designed for search and rescue missions, built for all-terrain mobility with enhanced stability to navigate rough surfaces where wheeled robots fail. Using inverse kinematics and a trot gait algorithm, it ensures precise and balanced movement. Equipped with IMU and ultrasonic sensors, it detects obstacles and adapts in real-time. This project aims to develop a highly agile and intelligent robot capable of autonomous navigation in hazardous environments, aiding in disaster response, exploration, and surveillance.

## Slide 4
LEARN . GROW . EXCEL
Literature Review
Sl.No | Title | Authors & Publications | Techniques Used and Observations
1 | “Intelligent Control of Multilegged Robot Smooth Motion: A Review" | YONGYONG ZHAO 1 , JINGHUA WANG 1,2, (Member, IEEE), GUOHUA CAO3 , YI YUAN1 , XU YAO1 , AND LUQIANG QI1 | This study presents gait optimization algorithm and motion planning with its core mechanical aspects from different patterns while it is found out that trot gait algorithm is more efficient.

## Slide 5
LEARN . GROW . EXCEL
Literature Review (Contd…)
Sl.No | Title | Authors & Publications | Techniques Used and Observations
2 | "ANYmal: A Dynamic Quadruped Robot" | Hutter et al., IEEE Robotics and Automation Letters (RAL), 2017 | ANYmal uses torque-controlled joints for agile locomotion. It is capable of autonomous terrain adaptation and energy-efficient movement, supported by real-time feedback from onboard sensors.
3 | "Cheetah 3: Blind Locomotion" | Kim et al., IEEE/RSJ IROS, 2018 | Cheetah 3 achieved blind locomotion using proprioceptive feedback and model-based control. The robot successfully navigates stairs and obstacles without relying on vision.

## Slide 6
LEARN . GROW . EXCEL
Literature Review (Contd…)
Sl.No | Title | Authors & Publications | Techniques Used and Observations
4 | "Vision-Assisted Quadruped Control" | Kolvenbach et al., Robotics and Automation Letters (RAL), 2019 | The sensor integration and perception improve the stability and decision-making of quadruped robots on complex terrains.
5 | BigDog: The Rough-Terrain Quadruped" | Raibert et al., IEEE Robotics and Automation, 2008 | BigDog uses hydraulic actuators and advanced dynamic stability control to navigate rough terrain. The robot successfully carried heavy loads, demonstrating robustness in extreme environments.

## Slide 7
LEARN . GROW . EXCEL
Literature Review (Contd…)
Sl.No | Title | Authors & Publications | Techniques Used and Observations
6 | “Dynamic locomotion of quadruped robots.” | K.Y. LEE and J.S.KIM | The sensor integration and perception improve planning of the different available gait algorithms.

## Slide 8
LEARN . GROW . EXCEL
METHODOLOGY
Concept & Design
Defined project objectives for a search and rescue quadruped.
Designed the robot’s mechanical structure from an open source.
Kinematics & Gait Planning
Developed inverse kinematics for precise leg movement.
Implemented a trot gait algorithm for stable locomotion.
Hardware Integration
Assembled components: Raspberry Pi, servo motors, ultrasonic sensors, and IMU (MPU6050).
Designed and tested electronic circuits for motor control and sensor interfacing.
ROS2 & Simulation
Developed custom ROS2 controllers for motion execution.
Used Gazebo for simulation before real-world testing.
Testing & Optimization
Conducting multiple real-world trials for stability and responsiveness.
Fine-tuned algorithms for efficient movement and obstacle avoidance.

## Slide 9: THEORETICAL CALCULATIONS
Inverse Kinematics Using DH Parameters:
To compute the joint angles (𝜃1, 𝜃2, 𝜃3) for each leg, we work backward from the desired foot position (𝑥,𝑦,𝑧) using the Denavit-Hartenberg (DH) parameters:
𝜃𝑖 (Joint angles – to be calculated)
𝛼𝑖 (Link twists)
𝑎𝑖 (Link lengths)
𝑑𝑖 (Link offsets)
Step 1: Solve for Hip Yaw Joint (𝜃₁)
Determines the rotation of the leg in the XY plane.
𝜃₁ = atan2(y, x)
Step 2: Solve for Hip Pitch and Knee Joints (𝜃₂, 𝜃₃)
Use the Law of Cosines to determine joint angles based on the distance r from the hip to the foot.

## Slide 10
Control Circuit
• Servo Motors to PCA9685 Driver: – 12 servo motors (3 per leg) are connected to the PCA9685 PWM driver board. – The board generates precise PWM signals to control each servo's position.
• PCA9685 to ESP32 Microcontroller: – The PCA9685 communicates with the ESP32 via the I2C interface. – The ESP32 serves as the central controller executing gait algorithms .
• Sensor Integration: – Ultrasonic sensors and an IMU provide real-time data for obstacle detection and stability. – These sensors feed information into the ESP32 for dynamic adjustments during locomotion.
• Power Supply Connections: – Variable power supply, regulated by a UBEC, delivers stable power to both the high-current servos and the microcontroller. – Separate power paths ensure that sensor and control circuits remain unaffected by servo power fluctuations.

## Slide 11: VALIDATION AND TESTING
IMU and ESP32 successfully tested Communication with the micro-ROS agent verified Raspberry Pi tested and confirmed to be functional Raspberry Pi successfully communicates with the ESP32 ROS2 nodes have been created to receive sensor data, ensuring real-time feedback from the hardware Currently developing embedded C code for gait planning, leveraging DH parameters as references to achieve efficient and stable locomotion

## Slide 12
Budgeting
• Motors (12 Servos): – 12 × ₹1500 = ₹18,000
• 3D Printing: – ₹5000 (Structural components using PLA+ at 30% infill)
• Controller & Sensors: – Raspberry Pi Bundle: ₹9400 – ESP32 Module: ₹650 – IMU Sensor: ₹270
– Motor Driver: ₹200
• Support Items: – Nuts, bolts, fasteners, etc.: ₹3000

## Slide 13
Duration Name of task | Week 1 | Week 2 | Week 3 | Week 4 | Week 5 | Week 6
Literature Survey |  |  | Completed |  |  | 
Data Collection | Completed | Completed | Completed |  |  | 
Design |  | Completed |  |  |  | 
Programming |  |  |  | Completed | To be Completed | 
Implementation |  |  |  |  |  | To be Completed

## Slide 15
References
"Quadruped Robot Design and Control: A Review" by L. B. Freeman, J. R. S. Gamboa, and D. H. D. Chien.
Boston Dynamics - Spot Robot
"The Roboticists Guide to the Control of Quadruped Robots" by Antonio Bicchi and Lorenzo Marconi.
"Quadruped Robot Locomotion: A Survey" by Sung-Min Kim and Joon Ho Choi.

## Slide 16
References
5. "The Development and Control of the Quadruped Robot LAURA" by M. J. Schmidt, J. E. DeRuntz, and R. A. Knepper
6. "Dynamic Locomotion of Quadruped Robots: Theory and Application" by K. Y. Lee, J. S. Kim, and H. Y. Lee